## Slide 1: Troubleshooting of Computer
Prepared by:
Amar Khanal

## Slide 2: 1. Computer is not turning on (no cpu fan and smps fan revolving)
Check if the AC outlet is not switched on
Check if the AC power cord is damaged (check using multi meter if there is continuity)
Check the power supply (SMPS) by connecting green wire of 20/24 pin cable with a black wire.
If SMPS is also OK please replace the motherboard
If the problem does not solve escalate it to senior professionals

## Slide 3: 2. The CPU fan and SMPS fan is revolving but no display in monitor
Check the keyboard and press NUM Lock if the light of Num lock toggles.
If it toggles check the display cable (VGA cable or HDMI cable) or the power cable of monitor, if not please check the monitor if it is faulty.
If the NUM lock doesnot toggle check for bad RAM stick.
Check the display card to be faulty.
If the problem still continues, check if it is motherboard or CPU issue, replace one at a time and test.
If the problem still doesnot solve escalate it to senior professional.

## Slide 4: 3. Your Personal Computer is Overheating. (Computer automatically turns off after some time
Check if the cpu fan is revolving or not.
Check the dust in cpu fan and in case of laptop check if there is some blockage in the air vents.
Check if the thermal paste of CPU is dry or not, if dry please change the thermal paste.

## Slide 5: 4. “No Bootable disk found”
This issue is majorly caused by two reasons: Bad OS or Bad HDD/SSD
Check if the HDD with OS is shown in the BIOS setting.
If it is shown then it is OS issue please repair the OS or reinstall it.
If it is not shown then please replace the HDD. (Note nowadays HDD are replaced with SSD’s)

## Slide 6: 5. PC Blue screen of death
This issue is caused by different factors like
Bad Memory or Bad motherboard
Corrupted OS
Hard drive failure (Near to dead)
Overheating
Corrupted or improper drivers
Trojans and viruses
Power related issues
Heavy task by user
So, please check from most obvious Corrupted OS to motherboard.
If the issue is periodic please install fresh OS in first step.

## Slide 7: 7. You cannot find 64-bit option in virtual box while installing Ubuntu 64-bit OS
It is because Virtualization is disabled in the BIOS
To solve it:
Goto BIOS setting
Search for Intel Virtualization Technology and enable it and for AMD x64: AMD SVM (Secure Virtual Machine) is enabled

## Slide 8: 8. HDMI Port is not working
Check if the hardware is physically damaged or not.
Change the HDMI cable
Reinstall the display driver
If above does not solve the issue please change the HDMI connector from the board, in case of desktop please change the display card.

## Slide 9: 9. Computer crashes before loading OS
Please reinstall the OS
If reinstalling doesnot solve the issue please change the HDD

## Slide 10: 12. Your read/write speed has decreased in SSD dramatically
Low Space
AHCI (Advanced Host Controller Interface) mode is disabled
The Boot sequence is incorrectly configured
Computer or SSD is infected with viruses
BIOS/firmware is outdated
Something is wrong with the SATA port or cable
Low RAM.

## Slide 11: Laptop charger light goes off after connecting to laptop
This case is of shorting of laptop motherboard
So, please remove the short of motherboard