## Slide 1: IPv4 Address Subnetting
Lecture 17
CT4005NI - Computer Hardware and Software
Architectures

## Slide 2
An IP address is a numeric identifier assigned to each machine on an IP network.
It is unique logical address that specifies where the device is on the network.
It is not hard-coded like mac-address i.e. it can change.
It has two types IPv4 and IPv6
172.16.0.12 192.168.1.1
2001:db8:3c4d:15::1a2f:1a2b
IP address

## Slide 3
It is 32-bit address represented in decimal.
If we see 192.168.1.1 its
11000000.10101000. 00000001.00000001
It is divided into four octets.
Maximum value in one octet = 11111111 =255
Minimum value in one octet = 00000000 =0
IPv4 (Internet Protocol version 4)

## Slide 4
Bit: A bit is one digit, either a 0 or a 1.
Byte: A collection of 8 bits equals to 1 byte.
Octet: An octet is made up of 8 bits.
Network address: This is the designation used in routing to send packets to a remote network.
Broadcast address: The address used by applications and hosts to send information to all nodes/hosts on a computer network.
IP Terminology

## Slide 5
Subnet Mask
  A subnet mask is a four-octet number used to identify the network ID portion of a 32-bit IP address.
  eg: 255.255.255.0
  In binary: 11111111.11111111.11111111.00000000
  Network Part Host part
  The part with 1’s is network part and with 0’s is host part.
  It is written with IP address to indicate the network the IP is associated with.

## Slide 6
Classes of IP address
Class | IP range | Subnet mask
Class A | 1.0.0.0 -126.255.255.255 | 255.0.0.0
Class B | 128.0.0.0 – 191.255.255.255 | 255.255.0.0
Class C | 192.0.0.0 -223.255.255.255 | 255.255.255.0
Class D | 224.0.0.0 -239.255.255.255 | Reserved for multicast
Class E | 240.0.0.0 -254.255.255.255 | Scientific research

## Slide 7
CIDR value (Classless Inter Domain Routing)
  CIDR value is the number of network bits in an IP address.
  If 192.168.1.0/24 then /24 is the network bit/CIDR in the IP address.
  so in binary: 11111111.11111111.11111111.0000000
  and subnet mask: 255.255.255.0

## Slide 8
Network Addressing

## Slide 9
Unicast, Broadcast and Multicast

## Slide 10
Binary to Decimal Conversion

## Slide 11
Decimal to Binary Conversion

## Slide 12
Problems with a single network

## Slide 13
The process of breaking down a single big broadcast domain into a
bunch of smaller ones.
Subnetting

## Slide 14
The network address is a unique address to identify the network portion of the IP network
It is the first IP of the network.
Network Address

## Slide 15
A broadcast address is used to send broadcast messages on the network.
It is the last IP of the network.
Broadcast Address

## Slide 16: Example: Solve 10.2.32.254/18
Binary Subnet mask: 11111111. 11111111.11000000.00000000
Subnet mask : 255.255.192.0
No of IP’s : 2^14=16,384
No of usable IP’s: 2^14 -2=16,384-2=16,382
Network ID: 10.2.0.0
Broadcast ID: 10.2.63.255
Usable range: 10.2.0.1 – 10.2.63.254

## Slide 17
On the End Devices
CONFIGURING COMPUTER_01 in the network topology:

## Slide 18
On the End Devices
CONFIGURING COMPUTER_02 in the network topology:

## Slide 19
On the Router

## Slide 20
Testing the Subnets
Pinging Computer_02 from Computer_01

## Slide 21: HAVE A NICE DAY